Computation
Power

---
Battle Royal Review
- Small resolution 32x22 on text screen
- Program based on Matt’s C64 version
- only 16 iterations/colours
- 16 bit fixed point (8.8) numbers
- BASIC65:	4.15 sec @40 MHz
- Assembler:	0.40 sec @40 MHz
[Speaker Notes: was designed to run on multiple 8bit platforms and used the lowest common festures]

---
High-Resolution
- using MEGA65 VIC-IV FCM mode
- 320x200 with 256 colours
- tile based graphics
- 48 iterations
- common optimizations
[Speaker Notes: 16 bit characters which are really pointers into flat memory reduce multiplications]

---
BASIC65
- simple conversion of LowRes version
- still uses floating point numbers
- makes use of advanced capabilities:
  - F018 DMA Controller for screen clear
  - CPU Math Acceleration Registers
[Speaker Notes: basic is designed to use the mega65s advanced features]

---
45GS02 Assembler
- learning VIC-IV
- 32 bit fixed point (8.24) numbers
- use of Math Acceleration Registers
- base page for variables and pointers
- Future enhancements
[Speaker Notes: Enhancements: timing via CIA use 32bit Q-Register opcodes math subroutine unrolling]